# Project RS.2

RS.2_Knjazevac-Razvoj (Serbia)

| Picture of the building Source: Construction cluster DUNDJER Nis, Serbia |  | Building Type |
| --- | --- | --- |
|  |  | Office |
|  |  | Building Phase |
|  |  | In use Date of Completion: 2005 |
|  |  | Building Characteristics |
|  |  | Total Floor Area: 340 m² Number of storeys: 3 |
|  |  | Address |
|  |  | Street Kej Dimitrija Tucovica 30 City Knjazevac COUNTRY Serbia |
| Ground plan of the building |  | Assessor |
|  |  | Name: Biljana Avramovic Company: Construction cluster DUNDJER Nis, Serbia |
|  |  | Building Owner |
|  |  | Name: Company: JP Direkcija Knjazevac |
|  |  | Architect |
|  |  | Name: Nebojsa Ivankovic Company: JP Direkcija, Knjazevac |
|  |  | Assessment Methodology |
|  |  | OPEN HOUSE v1.1 (01/2012) Basic & Quick Sustainability Assessment - Complete Sustainability Assessment |
| Section of the building Building designer: Dipl. Ing. Arch. Nebojsa Ivankovic |  |  |

Project description

Description of building project Main sustainability aspects (environmental, social/functional, economic, , process, location) (max. 500 words) Project description The case-study building hosts J.P. “Razvoj” (Public – Municipality - Enterprise “Razvoj”). The Enterprise supports urban development of Municipality Knjaževac, and controls public (municipal) investments, including design of major projects and objects. The Enterprise takes part in regional development and supports research in collaboration with closer research institutions, usually with University of Niš. The building is located in the downtown of city Knjaževac, in pedestrian zone, close to main administrative municipality institutions. Face of the building is west-southwest oriented, without shadowing obstacles. The view from the building front side is to the small city central park and river Timok. The building has 3 main floors and an attic. In the 3 floors are located offices, and in attic small conference hall, which is used also as a design studio for working team consultations. The reconstruction of building was accomplished in the year 2005, with steady improvement, especially in energy consumption. This is the only office building with heating/cooling system based on heat pump. In addition, there is design of using solar energy (PV system) on the south oriented part of the roof. The design draft for using PV solar energy shows ability for using 200 m2 (roof area) for PV panels After completing, it would enable saving of 15-20 % of total energy consumption. Modeling the thermal energy balance of buildings is recently a challenging task for local architects and engineers. Directive EPBD (2002/91/ES) is recently enforced by local Energy Law, but in the time of building design and construction, the elements of design like glazing areas or windows thermal characteristics, the climate zone, the orientation, and the type of construction (e.g. high or low thermal inertia) have not been considered in a way to optimize their thermal contribution to the whole building’s energy balance. The measuring system, necessary for proper assessment and improvement, has to be realized in near future. All the sustainability aspects (environmental, social/functional, economic, technical, process, location), are assessed “as is”, according to given scale. For Economic Quality assessment, the bill of quantities is now out of date, due to unrealistic prices of some materials and works, and using some not any longer used materials (with not standardized quality) and equipment with not strictly defined efficiency, and, finally, local rate of inflation (over 10 %). Sensitivity analysis, being considerable politically dependent, is even more complex, and somehow rather unpredictable. It is worthy to mention that this building was chosen, it seems, occasionally, and not as an example of good practice. The building is located in underdeveloped part of Serbia with all consequences to quality of building and, consequently, building sustainability. But, it is, in a way, representative case of construction technology in southeast Serbia.

Results

| RS.2 Knjazevac - Razvoj SERBIA |
| --- |
| 1 | Environmental Quality | Indicator Score % | Indicator Weight |
| 1.1 | Global Warming Potential (GWP) | 0 | 1 |
| 1.2 | Ozone Depletion Potential (ODP) | 0 | 1 |
| 1.3 | Acidification Potential (AP) | 0 | 1 |
| 1.4 | Eutrophication Potential (EP) | 100 | 1 |
| 1.5 | Photochemical Ozone Creation Potential (POCP) | 0 | 1 |
| 1.6 | Risks from materials | 0 | 2 |
| 1.7 | Biodiversity and Depletion of Habitats | 40 | 2 |
| 1.8 | Light Pollution | 100 | 2 |
| 1.9 | Non-Renewable Primary Energy Demands (PEnr) | 0 | 2 |
| 1.10 | Total Primary Energy Demands and Percentage of Renewable Primary Energy | 0 | 2 |
| 1.11 | Water and Waste Water | 10 | 3 |
| 1.12 | Land use | 50 | 3 |
| 1.13 | Waste | 10 | 3 |
| 1.14 | Energy efficiency of building equipment (lifts, escalators etc.) | 0 | 3 |
| 2 | Social / Functional Quality | Indicator Score % | Indicator Weight |
| 2.1 | Barrier-free Accessibility | 0 | 4 |
| 2.2 | Personal Safety and Security of Users | 7 | 4 |
| 2.3 | Thermal Comfort | 28 | 3 |
| 2.4 | Indoor Air Quality | 19 | 4 |
| 2.5 | Water Quality | 80 | 4 |
| 2.6 | Acoustic Comfort | 65 | 3 |
| 2.7 | Visual Comfort | 71 | 2 |
| 2.8 | Operation Comfort | 86 | 3 |
| 2.9 | Service Quality | 20 | 4 |
| 2.10 | Electro Magnetic Pollution | 50 | 4 |
| 2.11 | Public Accessibility | 100 | 4 |
| 2.12 | Noise from Building and Site | 100 | 3 |
| 2.13 | Quality of the Design and Urban Development of the building and Site | 0 | 4 |
| 2.14 | Area Efficiency | 100 | 3 |
| 2.15 | Conversion Feasibility | 44 | 2 |
| 2.16 | Bicycle Comfort | 0 | 2 |
| 2.17 | Responsible Material Sourcing | 0 | 2 |
| 2.18 | Local Material | 0 | 2 |
| 3 | Economic Quality | Indicator Score % | Indicator Weight |
| 3.1 | Building-related Life Cycle Costs (LCC) | 44 | 4 |
| 3.2 | Value Stability | 26 | 4 |
| 4 | Technical Characteristics | Indicator Score % | Indicator Weight |
| 4.1 | Fire Protection | 0 | 4 |
| 4.2 | Durability of the structure and Robustness | 50 | 4 |
| 4.3 | Cleaning and maintenance | 95 | 3 |
| 4.4 | Resistance against hail, storm high water and earthquake | 0 | 4 |
| 4.5 | Noise Protection | 10 | 4 |
| 4.6 | Quality of the building shell | 7 | 4 |
| 4.7 | Ease of Deconstruction, Recycling, and Dismantling | 3 | 3 |
| 5 | Process Quality | Indicator Score % | Indicator Weight |
| 5.1 | Quality of the Project’s Preparation | 31 | 4 |
| 5.2 | Integrated Planning | 100 | 4 |
| 5.3 | Optimization and Complexity of the Approach to Planning | 21 | 4 |
| 5.4 | Evidence of Sustainability during Bid Invitation and Awarding | 5 | 2 |
| 5.5 | Construction Site impact/ Construction Process | 0 | 3 |
| 5.6 | Quality of the Executing Contractors/Pre-Qualification | 50 | 3 |
| 5.7 | Quality Assurance of Construction Execution | 50 | 4 |
| 5.8 | Commissioning | 50 | 4 |
| 5.9 | Monitoring, Use and Operation | 36 | 3 |
| 6 | The Location | Indicator Score % | Indicator Weight |
| 6.1 | Risks at the Site | 91 | 2 |
| 6.2 | Circumstances at the Site | 71 | 2 |
| 6.3 | Options for Transportation | 25 | 4 |
| 6.4 | Image and Condition of the Location and Neighbourhood | 78 | 3 |
| 6.5 | Vicinity to amenities | 86 | 4 |
| 6.6 | Adjacent Media, Infrastructure, Development | 56 | 3 |