# Project RS.3

RS.3_Uni Campus_Nis (Serbia)

| Picture of the building Source: Construction cluster DUNDJER Nis, Serbia |  | Building Type |
| --- | --- | --- |
|  |  | 25% Office 75% Residential |
|  |  | Building Phase |
|  |  | In use Date of Completion: 2004 |
|  |  | Building Characteristics |
|  |  | Total Floor Area: 562 m² Number of storeys: 5 |
|  |  | Address |
|  |  | Street City Nis COUNTRY Serbia |
| Ground plan of the building |  | Assessor |
|  |  | Name: Prof. Dr. Djordje Djordjevic Company: Construction cluster DUNDJER Nis, Serbia |
|  |  | Building Owner |
|  |  | Name: Company: Condominium of owners |
|  |  | Architect |
|  |  | Name: A. Budjevac Company: Nisprojekt Nis, Serbia |
|  |  | Assessment Methodology |
|  |  | OPEN HOUSE v1.1 (01/2012) Basic & Quick Sustainability Assessment - Complete Sustainability Assessment |
| Section of the building |  |  |
| Assessment process |  |  |

Project description

Description of building project Main sustainability aspects (environmental, social/functional, economic, technical, process, location) (max. 500 words) The building taken as case-study is located in recently built settlement near complex of technical faculties of University Niš (Civil Engineering and Architecture, Mechanical Engineering, and Electronical Engineering). The settlement is named “Nikola Tesla” after famous Serbian scientist and inventor. The complex of residential and commercial buildings (L1-L20) is oriented in the direction east-northeast in compliance with zoning requirements. The complex is located in the northern part of city of Nis and consists of three groups of facilities GF +3 + PK (Attic). The building is residential-business (office) in relation 75:25. Residential part is devoted to university staff, and offices for supply and related activities. Vehicular access to the complex is from Boulevard Nikola Tesla and Boulevard 12. februara, and pedestrian (and bike ) from the direction of the fortress (downtown) and technical faculties. The building has 3-main floors (residential part), ground floor and basement (Office part), and attic. Office part, which is taken in consideration, is outward oriented, directly to the yard. Regarding technical measures which support building sustainability, in the time of building design and construction works, only necessary, by national regulations enforced measures, have been realized. For example, thermal insulation is realized in the following way. All the "sandwich" walls are thermally insulated with mineral wool insulation. All basement ceiling above which is a business area are covered with "mixed" panels. Sound insulation between rooms is achieved by special wall thickness (d = 23 cm) (both sides are plastered brick block of d = 19cm), and especially between residential and office space d = 20cm (+ plastering both sides 4cm). Floor structure of the final ceilings are covered by insulated panels of hard mineral wool. Floors on the ground are thermally isolated by "mixed" panels. All the sustainability aspects (environmental, social/functional, economic, technical, process, location), are assessed “as is”, according to given scale. The assessment process is realized in a way “as exact as possible.” The Economic Quality assessment is done very rough, by rough estimation. There are number of reasons for that. First of all, the (estimated) bill of quantities is now out of date, because of unrealistic prices of some materials and works, using some not longer used materials and equipment, and, finally, local rate of inflation (over 10 %). Sensitivity analysis is even more complex. It is worthy to mention that this building was chosen, it seems, occasionally, and not as an example of good practice. The design phase started immediately after NATO bombing of Serbia, as a part of country past-war reconstruction, and therefore, not strictly taking in account all sustainability aspects.

Results

| RS.3 UNI Campus - Nis SERBIA |
| --- |
| 1 | Environmental Quality | Indicator Score % | Indicator Weight |
| 1.1 | Global Warming Potential (GWP) | 0 | 3 |
| 1.2 | Ozone Depletion Potential (ODP) | 0 | 2 |
| 1.3 | Acidification Potential (AP) | 0 | 2 |
| 1.4 | Eutrophication Potential (EP) | 100 | 1 |
| 1.5 | Photochemical Ozone Creation Potential (POCP) | 0 | 1 |
| 1.6 | Risks from materials | 0 | 3 |
| 1.7 | Biodiversity and Depletion of Habitats | 40 | 4 |
| 1.8 | Light Pollution | 100 | 3 |
| 1.9 | Non-Renewable Primary Energy Demands (PEnr) | 100 | 2 |
| 1.10 | Total Primary Energy Demands and Percentage of Renewable Primary Energy | 50 | 3 |
| 1.11 | Water and Waste Water | 1 | 4 |
| 1.12 | Land use | 50 | 3 |
| 1.13 | Waste | 10 | 4 |
| 1.14 | Energy efficiency of building equipment (lifts, escalators etc.) | 0 | 4 |
| 2 | Social / Functional Quality | Indicator Score % | Indicator Weight |
| 2.1 | Barrier-free Accessibility | 0 | 4 |
| 2.2 | Personal Safety and Security of Users | 7 | 4 |
| 2.3 | Thermal Comfort | 28 | 4 |
| 2.4 | Indoor Air Quality | 19 | 4 |
| 2.5 | Water Quality | 80 | 4 |
| 2.6 | Acoustic Comfort | 65 | 4 |
| 2.7 | Visual Comfort | 71 | 4 |
| 2.8 | Operation Comfort | 86 | 3 |
| 2.9 | Service Quality | 20 | 4 |
| 2.10 | Electro Magnetic Pollution | 50 | 3 |
| 2.11 | Public Accessibility | 100 | 4 |
| 2.12 | Noise from Building and Site | 100 | 4 |
| 2.13 | Quality of the Design and Urban Development of the building and Site | 0 | 3 |
| 2.14 | Area Efficiency | 90 | 3 |
| 2.15 | Conversion Feasibility | 44 | 2 |
| 2.16 | Bicycle Comfort | 0 | 3 |
| 2.17 | Responsible Material Sourcing | 0 | 2 |
| 2.18 | Local Material | 0 | 2 |
| 3 | Economic Quality | Indicator Score % | Indicator Weight |
| 3.1 | Building-related Life Cycle Costs (LCC) | 44 | 3 |
| 3.2 | Value Stability | 30 | 3 |
| 4 | Technical Characteristics | Indicator Score % | Indicator Weight |
| 4.1 | Fire Protection | 0 | 4 |
| 4.2 | Durability of the structure and Robustness | 50 | 4 |
| 4.3 | Cleaning and maintenance | 90 | 4 |
| 4.4 | Resistance against hail, storm high water and earthquake | 100 | 4 |
| 4.5 | Noise Protection | 10 | 3 |
| 4.6 | Quality of the building shell | 3 | 4 |
| 4.7 | Ease of Deconstruction, Recycling, and Dismantling | 7 | 3 |
| 5 | Process Quality | Indicator Score % | Indicator Weight |
| 5.1 | Quality of the Project’s Preparation | 19 | 4 |
| 5.2 | Integrated Planning | 80 | 4 |
| 5.3 | Optimization and Complexity of the Approach to Planning | 31 | 4 |
| 5.4 | Evidence of Sustainability during Bid Invitation and Awarding | 5 | 3 |
| 5.5 | Construction Site impact/ Construction Process | 0 | 3 |
| 5.6 | Quality of the Executing Contractors/Pre-Qualification | 50 | 4 |
| 5.7 | Quality Assurance of Construction Execution | 50 | 4 |
| 5.8 | Commissioning | 50 | 4 |
| 5.9 | Monitoring, Use and Operation | 53 | 4 |
| 6 | The Location | Indicator Score % | Indicator Weight |
| 6.1 | Risks at the Site | 96 | 2 |
| 6.2 | Circumstances at the Site | 54 | 2 |
| 6.3 | Options for Transportation | 38 | 4 |
| 6.4 | Image and Condition of the Location and Neighbourhood | 78 | 3 |
| 6.5 | Vicinity to amenities | 78 | 4 |
| 6.6 | Adjacent Media, Infrastructure, Development | 56 | 2 |